## Slide 1
Crypto16
Coprocessor
A 16-Bit Hardware Datapath for Cryptographic Operations
Course: CSE 226 — Hardware Design | Zagazig University — Faculty of Engineering
• Ahmed Mahmoud Abdel Fattah • Ibraheem Shaaban Abdel Nabi
• Ahmed Abdel Fattah Elmallah • Ahmed Salah Abdel Majeed
• Ahmed Tharwat Salah • Wateen Walid Mohamed Baree
VHDL
Notes: 1

## Slide 2
Agenda
01
Problem Statement
Why do we need a crypto coprocessor?
02
System Architecture
Big picture — how all blocks connect
03
Control Unit
The brain: decoding 4-bit CTRL signals
04
ALU
7 arithmetic & logic operations
05
Shifter
ROR8, ROR4, SLL8 transformations
06
Nonlinear LUT (S-Box)
The heart of cryptographic security
07
Combinational Block
MUX, result selection & integration
08
Simulation & Testing
Verification strategy & waveforms
Notes: 2

## Slide 3
Why a Crypto Coprocessor?
⚡
General CPUs Are Slow
Standard processors handle encryption in software — slow, power-hungry, and exposed to timing attacks.
🔒
Security Needs Hardware
Dedicated hardware keeps keys isolated, executes in constant time, and resists side-channel attacks.
🎯
Our Solution: Crypto16
A 16-bit coprocessor in VHDL that handles ALU operations, bit shifts, and S-Box substitution in one integrated datapath.
Implemented entirely in VHDL • Modular design • Full testbench suite
Notes: 3

## Slide 4
System Architecture
Register File
16 × 16-bit
Combinational Logic Block
Entity | Type
crypto16_coprocessor | Structural
register_file | Sequential
combinational | Structural + Behavioral
control_unit | Behavioral
ALU | Combinational
shifter | Combinational
NonLinearLut | Combinational
Adder_16bit | Structural
Input Register
Reset
Clock
CTRL
Ra
Rb
Rd
Result
Notes: 4

## Slide 5
System Architecture
crypto16_coprocessor (Top Level)
Notes: 4

## Slide 6
Control Unit
The Brain — Decoding 4-bit CTRL into datapath signals
CTRL Range | sel_block | Selected Block | Sub-signal
0000 – 0111 | 00 | ALU | ctrl[2:0] → alu_op (3-bit)
1000 – 1010 | 01 | Shifter | ctrl[1:0] → shift_op (2-bit)
1011 | 10 | NonLinearLut | Direct selection
1100 – 1111 | 11 | NOP / Reserved | Output = 0x0000
Output Signals Generated
  sel_block (2-bit) → ALU / Shifter / LUT / NOP
  alu_op (3-bit) → Which ALU operation
  shift_op (2-bit) → Which shift operation
Key Design Decision
The control unit completely separates instruction decoding from execution. The combinational block never interprets CTRL directly — it only reads pre-decoded sel_block signals.
Notes: 5

## Slide 7
Arithmetic & Logic Unit (ALU)
alu_op | Operation | Description
000 | ADD | A + B via 16-bit ripple-carry adder
001 | SUB | A − B (two's complement: A + ~B + 1)
010 | AND | Bitwise A AND B
011 | OR | Bitwise A OR B
100 | XOR | Bitwise A XOR B
101 | NOT | Bitwise complement of A
110 | MOVE | Pass-through: Output = A
Ripple-Carry Adder
16 Full Adder primitives chained in series. Carry propagates from bit 0 → bit 15.
FA
FA
FA
FA
bit 0 ... bit 15
SUB uses: A + (NOT B) + 1
Undefined alu_op → Output = 0x0000
Fully Combinational • No clock required • Result available within propagation delay
Notes: 6

## Slide 8
Register File
16 × 16‑bit General‑Purpose Registers
  Storage array: reg_data (0 to 15).
  Asynchronous Reads:
ABus = reg[Ra], BBus = reg[Rb] – available i immediately, no clock delay.
  Synchronous Write:
On rising clock edge, if wrt = '1', result → r reg[Rd].
  Reset Behaviour:
Asynchronous: all 16 registers clear to 0 0x0000 immediately when res = '1'.
REGISTER ARRAY (16 × 16-bit)
R00
16-bit
0x0000
R01
16-bit
0x0000
R02
16-bit
0x0000
R03
16-bit
0x0000
R04
16-bit
0x0000
R05
16-bit
0x0000
R06
16-bit
0x0000
R07
16-bit
0x0000
R08
16-bit
0x0000
R09
16-bit
0x0000
R10
16-bit
0x0000
R11
16-bit
0x0000
R12
16-bit
0x0000
R13
16-bit
0x0000
R14
16-bit
0x0000
R15
16-bit
0x0000
Notes: 5

## Slide 9
Shifter Block
Fixed-pattern bit rotations & shifts — fundamental to lightweight ciphers
00
ROR 8
IN:
FF00
OUT:
00FF
Rotate right by 8 bits.
Upper and lower bytes swapped.
01
ROR 4
IN:
FF00
OUT:
0FF0
Rotate right by 4 bits.
Each nibble shifts one position rightward.
10
SLL 8
IN:
B38F
OUT:
8F00
Logical left shift by 8. Lower byte zeroed, upper = original lower.
Any other shift_ctrl code → Output = 0x0000 (NOP fallback — no undefined behavior)
Notes: 7

## Slide 10
Nonlinear LUT — S-Box
The heart of cryptographic security — nonlinear substitution
How It Works
1
Take lower 8 bits of ABus
LutIn[7:0]
2
Split into two nibbles:
Upper [7:4] → S_Box1
Lower [3:0] → S_Box2
3
Each nibble substituted
independently (4-bit → 4-bit)
4
Concatenate results → LutOut[7:0]
Upper 8 bits pass through unchanged
S-Box 1 (Upper Nibble)
In | Out
0 | 1
1 | B
2 | 9
3 | C
4 | D
5 | 6
6 | F
7 | 3
8 | E
9 | 8
A | 7
B | 4
C | A
D | 2
E | 5
F | 0
S-Box 2 (Lower Nibble)
In | Out
0 | F
1 | 0
2 | D
3 | 7
4 | B
5 | E
6 | 5
7 | A
8 | 9
9 | 2
A | C
B | 1
C | 3
D | 4
E | 8
F | 6
Notes: 8

## Slide 11
Combinational Block & MUX
ABus (16-bit)
BBus (16-bit)
ALU
7 ops
Shifter
3 ops
Non-linear
LUT
M
U
X
RESULT
Result Source Selection
sel_block | Source
00 | ALU Output
01 | Shifter Output
10 | LUT Output
11 | 0x0000 (NOP)
All 4 blocks run in parallel.
The MUX selects only ONE result
based on sel_block from Control Unit.
BBus (16-bit)
ABus (16-bit)
Control Unit
CTRL(4-BIT)
Result
Notes: 9

## Slide 12
Coprocessor integration
ALU
7 ops
Shifter
3 ops
Non-linear
LUT
M
U
X
Control Unit
Result
16 × 16
Register file
Input register
ABUS
Rb
Ra
CTRL
Rd
CTRL
BBUS
Crypto16 Coprocessor is a
16-bit VHDL datapath with a hybrid reset, combining register storage, control decoding, and ALU, shifter, and LUT execution in one design.
Reset
Clock
Notes: 9

## Slide 13
Timing Model
CLK
Phase A
Phase B ↑
Phase A
Phase A — Combinational Evaluation
  ABus & BBus read asynchronously from register file
  ALU / Shifter / LUT all compute simultaneously
  MUX selects result based on sel_block
  No clock needed — result available after propagation delay
Phase B — Sequential Commit (Rising Edge)
  Result written to registers[Rd] if wrt = '1'
  ctrl and Rd sampled into ctrl_temp / Rd_temp
  Hybrid reset: async assert, sync deassert (prevents metastability)
  wrt = '0' for ctrl = 0111 (NOP — write disabled)
Single-cycle datapath • Asynchronous reads • Synchronous writes
Notes: 10

## Slide 14
Verification & Testbench Strategy
Level 1 — Unit Testbenches
  Full_Adder_TB — single-bit carry logic
  Adder_16bit_TB — overflow, 0+0, 0xFFFF+1
  ALU_TB — all 7 ops + edge values
  Shifter_TB — all 3 shifts + undefined codes → zero
  NonLinearLut_TB — full 256-value sweep
  register_file_TB — reset, write-enable, read-back
Level 2 — Integration Testbenches
  combinational_TB — MUX switching, CTRL routing across all blocks
  crypto16_coprocessor_TB — end-to-end: write ops, execute, readback
Directed stimulus • Expected outcomes in inline comments • Waveform inspection in Active-HDL
Notes: 11

## Slide 15
Simulation Results
ALU
ADD
✓ PASS
A=0x0032, B=0x001E
→ 0x0050
AND
✓ PASS
A=0xF0F0, B=0x0F0F
→ 0x0000
XOR
✓ PASS
A=0xAAAA, B=0xAAAA
→ 0x0000
NOT
✓ PASS
A=0x00FF
→ 0xFF00
Shifter
ROR8
✓ PASS
A=0xABCD
→ 0xCDAB
ROR4
✓ PASS
A=0xABCD
→ 0xDABC
SLL8
✓ PASS
A=0xABCD
→ 0xCD00
Undef
✓ PASS
ctrl=1111
→ 0x0000
LUT (S-Box)
Input 0x00
✓ PASS
LutIn=0x00
→ 0x1F
Input 0x0FB
✓ PASS
LutIn=0x0B
→ 0x11
All 256 values
✓ PASS
Full sweep
→ All match table
Upper 8 bits
✓ PASS
ABus=0xFF12
→ Upper=0xFF pass-through
Notes: 12

## Slide 16
Top Level Results
Sample results
CTRL => B (LUT)
✓ PASS
LutIn=0xEF
→ 0x0F56
CTRL => A (SLL8)
✓ PASS
Shifter=Shiftin(7 downto 0) & x“00"
→ 0xFF00
CTRL => 0 (ALU addition)
✓ PASS
ABUS + BBUS
→ 0x0FEF
Notes: 12

## Slide 17
Design Strengths
◈
Highly Modular
Each block independently instantiable and testable. Swap or upgrade any unit without touching others.
◉
Structurally Explicit
Ripple-carry adder built from primitive full adders — every gate traceable for formal verification.
◐
Clean Separation
Storage, computation, and control are logically partitioned across distinct entities.
◯
Deterministic Reset
All registers clear to 0x0000 on reset. Undefined opcodes produce 0x0000. No undefined behavior.
◆
Three Crypto Classes
ALU + Shifter + S-Box in one integrated 16-bit datapath — covers arithmetic, diffusion, and confusion.
◇
VHDL Best Practices
Uses ieee.numeric_std throughout. Hybrid reset synchronizer prevents metastability.
Notes: 13

## Slide 18
Conclusion
What We Built
  Fully functional 16-bit cryptographic coprocessor in VHDL
  3 execution units: ALU (7 ops), Shifter (3 ops), LUT (S-Box)
  16×16-bit register file with async read / sync write
  Control unit decoding 4-bit opcodes into datapath signals
  Complete testbench suite at unit + integration level
What We Learned
  How dedicated hardware accelerates & secures cryptography
  Structural vs behavioral VHDL — when to use each
  Modular design: independent units → easier testing
  Bottom-up verification: test primitives before integration
  Role of S-Boxes in resisting linear & differential cryptanalysis
Crypto16 bridges basic digital logic and real-world cryptographic hardware design.
Notes: 14

## Slide 19
Thank You
Questions?
Team
Coprocessor Integration, Control Unit, Presentation
Ibraheem Shaaban Abdel Nabi
LUT, Report
Ahmed Tharwat Salah
Combinational Integration, Presentation
Ahmed Salah Abdel Majeed
Shifter, Schematic
Ahmed Abdel Fattah Elmallah
ALU, Schematic
Wateen Walid Mohamed Baree
Register file, Report
CSE 226 — Hardware Design • Zagazig University
Ahmed Mahmoud Abdel Fattah
Notes: 15